# Special Features:

- High speed with low noise

- Compact and efficient structure design

- Adjustable platform easy objects’ loading

- Infrared positioning system with aiming accuracy

- Water fill up alarm and automatic air ventilation device keep good working environment

| LD6050/ LD9060 / LD1612 Laser Engraving Machine |
| --- |
| Laser-Pro Engraver ·Adopts high quality straight-line guide. ·Fast and stable three-phase stepping motor ·High hardness alloy aluminums material with good parallel degree. ·Constant-current pulse width control circuit with high stability ·Advanced DSP control technology and SCSI interface ·Compatible with most sign-making software ·The lathe type frame guarantees the smoothness ·Be able to work on varieties of materials | ★Technical Parameters |
|  | Item | LD6050 | LD9060 | LD1612 |
|  | Laser Power | 60W | 60W / 80W | 80w |
|  | Max. Working Size | 600×500mm | 900x600mm | 1,600x1,200mm |
|  | Engraving Speed | ≤40m/s |
|  | Laser Type | Co2 glass laser machine |
|  | Min. Word Model | Chinese characters 2.5mm, English letter 1mm |
|  | Machine Power | <1,500W (without accessory) |
|  | Control Software | Laser Soft V4.0 |
|  | Distinguish Precision | 0.025mm |
|  | Orientation Precision | ±0.01mm |
|  | Carve Platform | The electric control platform |
|  | Temperature Request | 5℃～35℃ |
|  | Power Supply | 220V/50Hz |
|  | Dimension (L x W x H) NET/GROSS WEIGHT | 1,060x700x 1,000mm 126 / 193KG | 1,430X1,100X 950mm 237 / 322KG | 2,005x1,620x 1,100mm 400 / 532KG |
|  | Applicable Materials | Rubber plank, organic glass, plastics plank, dual-color plank, leather, artificial leather, cloth, timber, bamboo slice, ceramic, glass, compound crystal, fire-proof plank, cardboard and other nonmetal material. . |
|  | Unit Price(USD) | USD 7.500 | USD 9.000 / 9.800 | USD 17.000 |